## Slide 1: Safety
Week 5
Nov 16, 2020
G0A
G0B

## Slide 2: ZAP
  G0A01 Current flowing through the body cause a health hazard:
      By heating tissue

## Slide 3: Station Wiring
  A good way to guard against electrical shock at your station:
      Use three-wire cords and plugs for all AC powered equipment;
      Connect all AC powered station equipment to a common safety ground
      Use a circuit protected by a ground-fault interrupter
The National Electric Code regulates safety requirements for electrical wiring. G0B06
Common wire sizes for current capacity
AWG 16 10Amps
AWG 14 15 Amp G0B03
AWG 12 20 Amp. G0B02
AWG 10 30 Amp
In a 240 VAC single phase circuit both wires carrying the voltage should be protected with a circuit breaker. G0B01

## Slide 4: GFCI Ground Fault Circuit Interrupter
Current flowing from one or more of the voltage-carrying wires directly to ground will trip a GCFI
G0B05

## Slide 5: Back-up Power
Make sure you operate gas powered generators in a well ventilated area.
G0B09. G0B04
Disconnect the incoming utility power feed
G0B13.

## Slide 6: Power Supply Interlocks
Interlocks on power supplies and cabinets
Insure that dangerous voltages are removed if the cabinet is opened. G0B12

## Slide 7: Lightning
      Good for nearby lightning strikes
      Direct hits, forget it, kiss everything goodbye
  Avoid sharp bends in your grounding conductors.
Ground all protectors to a common plate. G0B11

## Slide 8: Overhead Tower Work
  Members of a tower work team should wear a hard hat and safety glasses at all times when any work is being done on the tower.
        On ground or up the tower
        Wear hard hat and safety glasses
8
G0B07 Confirm that the belt is rated for the weight of the climber and that it is within its allowable service life
G0B08. Make sure all circuits that supply power to the tower are locked out and tagged
  Putting on a climbing harness and safety
  glasses is a good precaution to observe before climbing an antenna tower.

## Slide 9
Antenna Work
For your safety Turn off the transmitter and disconnect the feed line prior to antenna work. G0B14
Ground mounted antennas should be installed such that it is protected against unauthorized access. G0A06

## Slide 10: RF Hazards

## Slide 11
RF Radiation
RF radiation is non-ionizing radiation
It does not cause genetic tissue damage.

## Slide 12: Exposure limits
  G0A03 Acceptable methods to determine that your station complies with FCC RF exposure regulations:
      By calculation based on FCC OET Bulletin 65
      By calculation based on computer modeling
      By measurement of field strength using calibrated equipment
Just remember all choices are correct

## Slide 13
Table 1 -- Power Thresholds for Routine Evaluation of Amateur Radio Stations
Band (Wavelength) Transmitter Power (W)
160 m 500
75 m 500
80 m 500
40 m 500
30 m 425
20 m 225
17 m 125
15 m 100
12 m 75
10 m 50
6 50
1.23 m 50
70 cm 70
33 cm 150
23 cm 200
13 cm and up 250

## Slide 14: Exposure limits
G0A08. Perform a routine RF exposure evaluation to ensure compliance with RF safety regulations when transmitter power exceeds levels specified in FCC Part 97.13
      G0A09 A calibrated field strength meter can be used to accurately measure the strength of an RF Field

## Slide 15
  Factors affecting the RF exposure of people near an amateur station antenna:
      Frequency and power level of the RF field
      Distance from the antenna to a person
      Radiation pattern of the antenna
15
Controlled
Uncontrolled
Take precautions to ensure that the antenna cannot be pointed in the direction of neighbors if excess of allowable exposure. G0A10

## Slide 16: Exposure Prevention
Indoor antennas: Make sure that MPE limits are not exceeded in occupied areas. G0A11

## Slide 17: Duty Cycle
  Duty cycle is one of the factors used to determine safe RF radiation exposure levels because it affects the average exposure of people to radiation.
G0A07 A lower transmitter duty cycle permits greater short-term exposure levels
17

## Slide 18
Soldering
Danger from lead-tin solder
G0B10
Lead can contaminate food if hands are not washed carefully after handling the solder