## Slide 1: Lesson 5
G. West
Your First Radio p. 65
Your Computer goes Digital p. 109
Multi-mode Radio Excitement p. 119
Run Some Interference Protection p. 131

## Slide 2: Lesson 5
Amateur Radio equipment
G. West
Your First Radio p. 73
Your Computer goes Digital p. 119
Multi-mode Radio Excitement p. 127
Run Some Interference Protection p. 137
ARRL: Ch. 2.3, 3.3, 5
3/2/19

## Slide 3
Generalized Transceiver Categories
Single Band
  Dual Band
    Multimode
      Multiband
        Handheld (HT)
Notes: In this lesson you will be comparing and contrasting the different kinds of equipment available. You can adjust these categories to meet your personal preferences and experiences. It would be a good idea to have examples of the different kinds of equipment. Catalogs from the major equipment retailers would be helpful to give an idea of the level of costs. Go ahead and deviate from any kind of lesson script during this lesson but keep in mind the time and keep from spending too much time on this topic.

## Slide 4
Basic Station Organization
Station Equipment
  Transmitter
  Receiver
  Antenna
  Power Supply
Accessory Station Equipment
Notes: Go over with the students the basic outline of the material to be presented during this lesson. This lesson is deceptively simple because there is a lot of preparation required to make this lesson effective. You should try to set up an operative station to give some demonstration contact. Use some care that you don’t set up a station that will intimidate the students on the first day, try to set up a station that would be typical of the type of station that they might set up in the beginning of their ham radio careers. Don’t spend a lot of time at this point demonstrating all the exotic modes available to the students, there will be plenty of time to do that later in the course. I would suggest a basic two meter set up and give demonstration contacts on repeaters and simplex. Then have a simple HF station and make one or two phone and one CW contact. Some advice on contact…don’t depend on a CQ being answered, it may or may not happen. I would suggest you have a few “planted” contacts from your club. These planted contacts are standing by on the frequency ready to step in and make a contact just in case your CQ goes unanswered. Try to get planted contact operators who are good at drawing out conversations on the radio. New operators are intimidated by radio and sometimes need to be prodded to say more than yes or no answers to questions.

## Slide 5
Transmitter
Receiver
Basic Radio Station
Transceiver
Power
Supply
TR
Switch
Antenna
T7A02 A transceiver combines the functions of a transmitter and a receiver

## Slide 6
What Happens During Radio Communication?
Transmitting (sending a signal):
  Information is converted to electronic form.
Transmitter
Info
For class,
What kind of info?

## Slide 7
What Happens During Radio Communication?
Receiving end:
Receiver
front end

## Slide 8
Demodulator
Detector
Modulator
Filters
Mixer
Amplifier
Oscillator
Produces a steady signal at a single frequency
Makes signals stronger
Converts a radio signal from one frequency to another.
T7A03
Removes information from modulated RF
Removes or blocks unwanted signals
Puts information on the RF signal
T7A08
Product
Detector
Detects CW & SSB
Frequency
Discriminator
Removes information from FM signals
Converts modulated RF
directly into data or voice
T7A05
Our Basic Building Blocks

## Slide 9: The Superheterodyne Receiver Block Diagram
The mixer combines two signals to
To convert one frequency to another, T7A03
One mixer = single conversion
Two mixers = double conversion

## Slide 10: Icom IC-7410
Mode Select
Band select
VFO, Tuning Knob, T4B02 Used for frequency entry
T4Bo4 Memory controls
Quick access to favorite frequencies.
AGC, automatic gain control, To keep received audio relatively constant T4B12

## Slide 11: Icom-7410
RIT Receive incremental tuning
T4B06 T4B07. change receive freq.
Noise blanker T4B05, T4B13
Help to eliminate
noise
Antenna tuner
Squelch T4B03 Mutes receiver
output when no signal.
T4B09 Filters, 2.4 kHz for SSB
T4B10 500 Hz for CW
T4B08 Some variable.

## Slide 12: Yaesu FT-60
Squelch
Memory or VFO operation
F + Select type of tone
Tuning control
F + Select tone frequency
Microphone
Select memory CH
or Frequency
Direct frequency entry
In VFO operation
ARO Automatic Repeater Offset
“PTT” Push to talk
T7A07
Scan function, scan through a range of frequencies to check for activity T4B14

## Slide 13: Increase Handheld output power
T7A10 An RF power amp can be used to increase power out
SSB/CW-FM switch sometimes found to set amplifier for proper mode. T7A09

## Slide 14
Nice to have handheld accessories
Extra battery packs.
Drop-in, fast charger.
Extended antenna.
External microphone and speaker.
Headset.

## Slide 15: Receivers

## Slide 16: Selectivity / Sensitivity
Selectivity – The receivers ability to
Discriminate between multiple signals. T7A04
Sensitivity – The ability to receive and detect the presence of a signal.
T7A01

## Slide 17
Increase Sensitivity
Receiver
Pre
Amplifier
T7A11

## Slide 18
HF Transceiver
On 28 MHz
Transverter
222 MHz
28 MHz in and out
222MHz
Transverter is used to extend the the frequency
Capabilities of a HF transceiver.
Example 1: A Transverter is being used to allow the HF transceiver to
operate on the 222MHz band.
Antenna connection
Transverter
T7A06

## Slide 19: Radio Frequency Interference RFI
RFI
Causes
T7B03
Fundamental overload
Harmonics
Spurious Emissions
Extra signals produced by all transmitters
Amateur Radio Station
RFI
Noise Sources
If it is related to electricity, it produces noise.
Good station practice. Ensure your station is not producing interference.

## Slide 20: RFI
Part 15 rules,
Covers un-Licensed devices that use RF communications.
May not cause interference to licensed equipment
Must accept interference caused by licensed equipment operating properly under FCC rules
Part 15 An unlicensed device that may emit low-powered radio signals on frequencies used by a licensed service. T7B09

## Slide 21: RFI
What would cause a broadcast AM or FM radio to receive an amateur radio transmission unintentionally? T7B02
The receiver is unable to reject strong signals outside the AM or FM band

## Slide 22: Filters
Overload interference by amateur to television T7B05
Check your radio equipment;
Make sure that your station is functioning properly and that it does not cause interference to your own radio or television T7B06
Filter out what you don’t want
Telephone from my amateur radio. T7B04
Put a RF filter on the telephone
Block the amateur signal with a filter at the antenna input of the affected receiver
Overload to a VHF transceiver from a nearby FM broadcast station T7B07
Band-reject filter
I don’t want interference to:

## Slide 23
Ferrite filter chokes
Distorted audio caused by RF current on the shield of a microphone cable? T4A09
Install a ferrite choke

## Slide 24: T7B08 What should you do if a "Part 15" device in your neighbor’s home is causing harmful interference to your amateur station?
  Work with your neighbor to identify the offending device
  Politely inform your neighbor about the rules that require him to stop using the device if it causes interference
  Check your station and make sure it meets the standards of good amateur practice
  All of these choices are correct

## Slide 25
T7B12
What might be the first step to resolve cable TV interference from your ham radio transmission?
Add a low pass filter to the TV antenna input
B. Add a high pass filter to the TV antenna input
C. Add a preamplifier to the TV antenna input
D. Be sure all TV coaxial connectors are installed properly
(D)

## Slide 26: Digital Communications
Protocol
Packet
PSK31
MFSK
RTTY
Keyboard to Keyboard
Many of the digital modes use error detection and correction.
T8D11 ARQ. Automatic Repeat Request
T8D08 Packet includes in the transmission
Check Sum for error detection
Header for sender’s and receiver’s information
Automatic repeat request in case of errors.
✔
A method for encoding, packaging, exchanging, and decoding digital signals

## Slide 27
T8D01 (D)
Which of the following is a digital communications mode?
A. Packet radio
B. IEEE 802.11. (Routers, LAN)
C. JT65
D. All of these choices are correct

## Slide 28: Digital Communications
Keyboard to Keyboard
Most popular in the HF Bands
Found at the bottom of the bands just above CW
PSK31 most used mode on HF.
Phase Shift Keying 31 baud T8D06
Sends Data at a slow rate

## Slide 29: Digital Communications.
APRS
Automatic Packet Reporting System T8D02
Basically a packet station connected to a
GPS Global Positioning System T8D03

## Slide 30
T8D05. Providing real-time tactical digital communications in conjunction with a map showing the locations of stations
APRS

## Slide 31
Mesh Network
IEEE 802.11 A Wi-Fi digital standard.
Broadband-Hamnet T8D12
Or, High Speed multi-media network
An amateur-radio-based data network using commercial Wi-Fi gear with modified firmware

## Slide 32
Computers
T4A02
A. For logging contacts and contact information
B. For sending and/or receiving CW
C. For generating and decoding digital signals

## Slide 33: Computer control
33
  T8D09 The code used when sending CW in the amateur bands is International Morse.
    T8D14 Can be sent using a hand key, electronic keyer or computer
  T8D10 Digital mode software
    WSJT was designed for weak signal computer / radio operation as in:
    A. Moonbounce or Earth-Moon-Earth B. Weak-signal propagation beacons C. Meteor scatter
  T8D13 FT8 digital mode
    A digital mode capable of operating in low signal-to-noise conditions that transmits on 15-second intervals

## Slide 34: Digital Modes Station Set UP
The connection between the transceiver and computer
T4A06 Receive audio, transmit audio, and push-to-talk (PTT)
T4A07 The sound card provides audio to the radio's microphone input and converts received audio to digital form
Transceiver
Computer
Soundcard
interface
Computer control
Microphone of line input T4A04
Most modern transceivers have built in soundcards and usb connections to connect to the computer

## Slide 35: Gateways
T8C11 A gateway is used to connect other amateur
radio stations to the internet

## Slide 36: Power Up
T6D05 A regulator is part of a power supply to maintain a stable voltage.
A power supply is a device that supplies electrical energy to
one or more electric loads.
T4A01 In selecting a power supply you must consider all of the following.
A. Efficiency of the transmitter at full power output
B. Receiver and control circuit power
C. Power supply regulation and heat dissipation
T4A10 A high-pitched whine that varies with engine speed in a mobile transceiver’s receive audio, is usually caused by the vehicles alternator.

## Slide 37: Power Up
T5A06 Mobile radio equipment uses a 12 volt power source.
T4A11 The negative return connection of a mobile transceiver power cable should be connected At the battery or engine block ground strap
Mobile equipment
T4A03 Use heavy gauge wire to avoid voltage falling below that needed for proper operation

## Slide 38: For Next Week
Study flash cards www.hamexam.org
73
Tom and Jack
Lesson 1
T1B
T3B
T8A
Lesson 2
T1A
T1C
TID
T1E
T1F
Lesson 4
T3A
T3C
T9A
T9B
T7C
Lesson 5
T4A
T4B
T7A
T7B
T8D
Lesson 6
T5A
T5B
T5C
T5D
T6A
T6B
T6C
T6D
T7D
Lesson 3
T2A
T2B
T2C
T8B
T8C
Lesson 7
T0A
T0B
T0C
Radio
Fundamentals
Rules &
Regs.
Comm. w/
Others
Antennas
Propagation
Equipment
Electricity
Safety